Graphs One Access Points Two UAVs

Configurations
Fixed Parameter	Value
Network AP Location	0,0 m
STA1 Location	1,1 m
STAs Locations	10,10m
Frequency	5GHz
Number of STAs	2
Traffic Type	UDP
STA 1 Traffic Data Rate	5Mbps
STA 2 Traffic Data Rate	50Mbps
MCS Value of DataRate / (MCS5)	wifi.SetRemoteStationManager("ns3::ConstantRateWifiManager", / "DataMode", StringValue("HeMcs5"), / "ControlMode", StringValue("HeMcs0"));
Channel Settings	50, 160, BAND_5GHZ, 0
Access Category Wifi6	AX
Simulation Time	10s
Propagation Loss Model	Default YansCHannel Loss Model

MCS Table

Results Table
Results:
Access Point at Location 10,10
UAV1 Transmitter Node at 1,1 meters
UAV2 Transmitter Node at 10,10 meters
UAV 1 Static
UAV2 Moving Away

.

Results Analysis UAV1 ( Fixed Location but UAV2 Moved Away and Impacts on UAV1 a little)

Analysis UAV2 ( UAV2 Moves Away and UAV1 Static)

.

UAV1 Data:

Throughput(Mbps)	Delay(s)	Jitter(s)	QoS	RSSI Value / (dBm)	Distance From AP
5.09505	0.00016474	0.000126506	1.01901	-35	1.4
5.09506	0.000180214	0.000143511	1.01901	-35	1.4
5.09471	0.000495536	0.000427242	1.01894	-35	1.4
5.09506	0.000258826	0.0002085	1.01901	-35	1.4
5.09416	0.000897354	0.000913462	1.01883	-35	1.4
5.09362	0.000749084	0.000786326	1.01872	-35	1.4
5.09488	0.00107788	0.00103454	1.01898	-35	1.4
5.09506	0.000088311	0.0000134928	1.01901	-35	1.4
5.09506	0.0000882225	0.0000132386	1.01901	-35	1.4

.

UAV2 Data:

Throughput(Mbps)	Delay(s)	Jitter(s)	QoS	RSSI Value	Distance From AP
50.8968	0.000200461	0.0000680681	1.01794	-65	14
50.8965	0.000238734	0.0000965413	1.01793	-76	17
50.8561	0.00656082	0.000424252	1.01712	-68	18.5
50.8924	0.000920942	0.000286555	1.01785	-68	19.2
10.72	3.63	0	0.21	-68	19.8
4.96023	3.73035	0.00201776	0.0992046	-68	20.1
0.15691	3.87901	0.0514474	0.00313819	-69	20.6
0	0	0	0	-71	22
0	0	0	0	-74	25