Data-rate Effect One Access Points Two UAVs

Configurations
Fixed Parameter	Value
Network AP Location	0,0 m
STA1 Location	1,1 m
STAs Locations	13,13m
Frequency	5GHz
Number of STAs	2
Traffic Type	UDP
STA 1 Traffic Data Rate	90Mbps,60Mbps,40mbps, 20Mbps,10Mbps,5Mbps
STA 2 Traffic Data Rate	90 Mbps
MCS Value of DataRate / (MCS5)	wifi.SetRemoteStationManager("ns3::ConstantRateWifiManager", / "DataMode", StringValue("HeMcs5"), / "ControlMode", StringValue("HeMcs0"));
Channel Settings	50, 160, BAND_5GHZ, 0
Access Category Wifi6	AX
Simulation Time	10s
Propagation Loss Model	Default YansCHannel Loss Model

MCS Table

Animation File:

Results Table
Results:
Access Point at Location 0,0

UAV1 Transmitter Node at 1,1 meters

UAV2 Transmitter Node at 13,13 meters

UAV 1 Static ( Data Rate Demand of UAV1 will effect QoS of UAV2)

UAV1 Data

Throughput(Mbps)	Delay(s)	Jitter(s)	QoS	Access Point UAV Distance	Demand(Mbps)
91.6324	0.00134823	0.000189139	1.01814	1.41	90
1.41	0.00121926	0.000285316	1.01805	1.41	60
1.41	0.00118481	0.000425213	1.01822	1.41	40
1.41	0.00121171	0.000771547	1.01821	1.41	20
1.41	0.00122625	0.000980159	1.01848	1.41	10
1.41	0.00130834	0.00119395	1.01897	1.41	5

UAV2 Data

Throughput(Mbps)	Delay(s)	Jitter(s)	QoS	Distance (m)	Deamand(mbps)
59.6826	1.53849	0.000361469	0.66314	19	90
62.386	1.43976	0.000347251	0.693178	19	90
66.1774	1.29715	0.000327409	0.735304	19	90
73.2222	1.02743	0.000296311	0.81358	19	90
76.6782	0.821218	0.000284938	0.85198	19	90
80.491	0.57962	0.00027707	0.894344	19	90